SCChart Controller - Basic design

Page / - last modified by sna on 2014/08/13 02:54

Basic design
last modified by sna
on 2014/08/13 02:54

Table of Contents
Mutual Exclusion
Normal segments
Kicking Horse Pass
Train controller
Structure
Station-2-Station controller
Structure
Dynamic Controller
Dynamic Scheduling

  - Mutual Exclusion
    - Normal segments
    - Kicking Horse Pass
  - Train controller
    - Structure
  - Station-2-Station controller
    - Structure
  - Dynamic Controller
    - Dynamic Scheduling
We compose our railway controller from several train controllers, combined with controllers for mutual exclusion.
## Mutual Exclusion
### Normal segments
For each block we generate one mutex controller, similar to the following pattern.

For each controlled train one state and the corresponding transitions are added.
A train must signal the wish to enter a segment by setting the variable bool <segment>_req[trainNum] to true.
The right to enter a segement is given to the train by setting the variable int <segment>_perm to the train number.
After leaving a segment the train must remove its request by setting <segment>_req[trainNum] to false again.
For a free track the *_perm variable is set to -1 and all tracks, apart from starting positions, are initialized with -1. For the starting positions the *_perm variables are set to the corresponding train number and the *_req variable for the train is set to true.
A train must not enter a segment or alter the settings of a segment without holding the lock for the segment. No exceptions from this rule are allowed.
### Kicking Horse Pass
To prevent collisions on the track, a special controller manages the rights to enter or leave the Kicking Horse Pass.

The controller splits the pass into two parts, left and right, corresponding to the track layout chart. (Simplified track layout)
Each part has two operational modes, in and out, being active when trains are allowed to either enter or leave the pass. When entering the pass the controller counts the entering trains and only lets two trains enter (one after the other). When leaving the pass the trains are removed from the counter, freeing space for the next train.
## Train controller
Each train controller is set in a separate region with a referenced state. This state has the following interface:

 input int *_perm; # All permission variables (Tracks) input bool *_perm # KH permission variables input int trainNum; input bool cleanup; input bool debug; output bool *_req[]; # All request variables
The train controller is composed of several Station-2-Station controllers. These are combined to form a complete schedule. Additionally, the cleanup signal has to be watched to abort the schedule and return back to the initial position.
### Structure
//
// Structure of a train controller based on test case 2
//
scchart Test2 "Test of IC_JCT" {
  // Set of request variables for all tracks for 11 trains
  bool IC_JCT_0_req[11], IC_LN_0_req[11], IC_LN_1_req[11], IC_LN_2_req[11];
  bool IC_LN_3_req[11], IC_LN_4_req[11], IC_LN_5_req[11], IC_ST_0_req[11];
  bool IC_ST_1_req[11], IC_ST_2_req[11], IC_ST_3_req[11], IC_ST_4_req[11];
  bool IO_LN_0_req[11], IO_LN_1_req[11], IO_LN_2_req[11], KH_LN_0_req[11];
  bool KH_LN_1_req[11], KH_LN_2_req[11], KH_LN_3_req[11], KH_LN_4_req[11];
  bool KH_LN_5_req[11], KH_LN_6_req[11], KH_LN_7_req[11], KH_LN_8_req[11];
  bool KH_ST_0_req[11], KH_ST_1_req[11], KH_ST_2_req[11], KH_ST_3_req[11];
  bool KH_ST_4_req[11], KH_ST_5_req[11], KH_ST_6_req[11], KIO_LN_0_req[11];
  bool KIO_LN_1_req[11], OC_JCT_0_req[11], OC_LN_0_req[11], OC_LN_1_req[11];
  bool OC_LN_2_req[11], OC_LN_3_req[11], OC_LN_4_req[11], OC_LN_5_req[11];
  bool OC_ST_0_req[11], OC_ST_1_req[11], OC_ST_2_req[11], OC_ST_3_req[11];
  bool OC_ST_4_req[11], OI_LN_0_req[11], OI_LN_1_req[11], OI_LN_2_req[11];
  bool req_in_R, req_out_R, req_in_L, req_out_L;
  // Set of permission variables for all tracks
  int IC_JCT_0_perm, IC_LN_0_perm, IC_LN_1_perm, IC_LN_2_perm;
  int IC_LN_3_perm, IC_LN_4_perm, IC_LN_5_perm, IC_ST_0_perm;
  int IC_ST_1_perm, IC_ST_2_perm, IC_ST_3_perm, IC_ST_4_perm;
  int IO_LN_0_perm, IO_LN_1_perm, IO_LN_2_perm, KH_LN_0_perm;
  int KH_LN_1_perm, KH_LN_2_perm, KH_LN_3_perm, KH_LN_4_perm;
  int KH_LN_5_perm, KH_LN_6_perm, KH_LN_7_perm, KH_LN_8_perm;
  int KH_ST_0_perm, KH_ST_1_perm, KH_ST_2_perm, KH_ST_3_perm;
  int KH_ST_4_perm, KH_ST_5_perm, KH_ST_6_perm, KIO_LN_0_perm;
  int KIO_LN_1_perm, OC_JCT_0_perm, OC_LN_0_perm, OC_LN_1_perm;
  int OC_LN_2_perm, OC_LN_3_perm, OC_LN_4_perm, OC_LN_5_perm;
  int OC_ST_0_perm, OC_ST_1_perm, OC_ST_2_perm, OC_ST_3_perm;
  int OC_ST_4_perm, OI_LN_0_perm, OI_LN_1_perm, OI_LN_2_perm;
  bool perm_in_R, perm_out_R, perm_in_L, perm_out_L;

  // Debug flag for additional output
  bool debug = false;
  // Cleanup flag for halting the trains at home station tracks
  bool cleanup = false;
  // Variable, that gives the number of trains to C-Controller for stability check
  int trainCount;

  // Set of constants for binding to referenced SCCharts
  const int c_EINS = 1;
  const int c_ZWEI = 2;
  const int c_DREI = 3;
  const int c_VIER = 4;
  const int c_FUENF = 5;

  // State initializing the trains on corresponding tracks
  initial state init references initRailway11Trains
  --> run;

  // State handling the train schedules
  state run {
    // Regions handling the mutual exclusion on the track segments
    region Mutexes:
      // State referenced to the MutexController for 11 Trains
      initial state Mutexes references mutexRailway11Trains;

    region KH_Mutexes:
      // State referenced to additional MutexController for KH
      initial state KH_Mutexes references kh_mutex;

    // Regions that contain the schedules for individual trains
    //--------------------------------------------------------------------------------------
    // Region with schedule for train 4
    region Train4 :
      // State with the schedule for train 4
      initial state train4 {

        // Annotation for replacing following constant in the hostcode of referenced SCChart
        @alterHostcode
        // Number of the train for identifying on track segments
        const int trainNum = 4;
        // Variable specifying the track, where the train arrives at,
        // and for transmitting the track number to next Station-2-Station controller
        int arrivalTrack = 3;

// Schedule of train 4: train drives only in the IC, should use station track 3
        // State Round referenced to ICIC Station-2-Station controller
        initial state Round references ICIC
          bind depTrack to arrivalTrack,
               destTrack to c_DREI,
               arrTrack to arrivalTrack
        // Transition to checking state
        >-> Choice;

        // State for checking, when the train should halt and if the train is on corresponding track
        state Choice
        // Transition for driving additional circle, if cleanup = false or wrong track used
        --> Round with !cleanup | !(arrivalTrack == 3)
        // Transition to final state
        --> Done;

        final state Done;
      };
    // Region with schedule for train 5, identical to region above
    region Train5 :
      initial state train5 {

        @alterHostcode
        const int trainNum = 5;
        int arrivalTrack = 2;

        initial state Round references ICIC
          bind depTrack to arrivalTrack,
               destTrack to c_ZWEI,
               arrTrack to arrivalTrack
        >-> Choice;

        state Choice
        --> Round with !cleanup | !(arrivalTrack == 2)
        --> Done;

        final state Done;

      };

    // Region with schedule for train 9, identical to region above
    region Train9 :
      initial state train9 {

        @alterHostcode
        const int trainNum = 9;
        int arrivalTrack = 1;

        initial state Round references ICIC
          bind depTrack to arrivalTrack,
               destTrack to c_EINS,
               arrTrack to arrivalTrack
        >-> Choice;

        state Choice
        --> Round with !cleanup | !(arrivalTrack == 1)
        --> Done;

        final state Done;
      };
    // Region with schedule for train 7
    region Train7 :
      initial state train7 {

        @alterHostcode
        const int trainNum = 7;
        int arrivalTrack = 1;

        // Schedule of train 7: train drives from OC-Station track 1 to IC-Station track 2 and back
        // arrivalTrack used for transmitting the number of station track where train arrived on
        // to next controller where the train starts on
        initial state OCtoIC references OCIC
          bind depTrack to arrivalTrack,
               destTrack to c_ZWEI,
               arrTrack to arrivalTrack
        // Transition to next Station-2-Station controller
        >-> ICtoOC;

        state ICtoOC references ICOC
          bind depTrack to arrivalTrack,
               destTrack to c_EINS,
               arrTrack to arrivalTrack
        // Transition to checking state because train at home station
        >-> Choice;

        // State for checking, when the train should halt and if the train is on corresponding track
        state Choice
        // Transition for driving additional circle, if cleanup = false or wrong track used
        --> OCtoIC with !cleanup | !(arrivalTrack == 1)
        // Transition to final state
        --> Done;

        final state Done;
      };
  };
}

## Station-2-Station controller
Each Station-2-Station controller realizes the movement from one of the stations (IC,OC,KH) to another station. All controllers using IC or OC parts have to respect the traveling directions. For the Kicking Horse Pass two separate controllers, forwards and backwards, are used.
The controllers starting from Kicking Horse Pass Station make an assumption of the direction of the train. These are dependent on the directions of the inner or outer circle, e.g. the KHIC controller starts backwards because this is the only valid direction to travel this path. To drive a train from the Kicking Horse Station (facing forward) to the Inner Circle we have to combine the KHOC and OCIC controllers.

When arriving on a station the train controller must first call the function void railArrival(int train, int station). This starts the waiting timer for the train.
Next the train must wait for int railDeparture(int train) to return 1.
After the waiting has finished the controller can reach a final state and pass the control back to the train controller.
### Structure
//
// Structure of a Station-2-Station controller from Station * to Station *
//
scchart STST " * to * Controller " {
  // Set of permission variables for required tracks
  input int *_perm;
  // Set of request variables for required tracks for 11 trains
  output bool *_req[11];
  // Train number
  input int trainNum;
  // Number of the departure track in a station
  input int depTrack;
  // Number of the destination track in a station
  input int destTrack;
  // Cleanup flag for selecting the destination track
  input bool cleanup;
  // Debug flag for additional output
  input bool debug;
  // Arrival track
  output int arrTrack;
  // Variable with value for arrTrack for selecting correct station elements
  int i_arrOnTrack;
  // Handles departing from a station *
  initial state *_ST {
    // hostcode call for additional output when debug
    entry debug / 'println([trainNum][ST-ST] ... )';
    // State, which sets requests for needed tracks
    initial state waitForPerm {
        entry / *_ST_4_req[trainNum] = true;
        entry / *_LN_0_req[trainNum] = true;
    }
    // Transition is taken, if all permissions are received
    --> gotPerm with (*_ST_4_perm == trainNum) & (*_LN_0_perm == trainNum)
    // Transition is taken, if some (not all) permissions are received
    --> backOff with (*_ST_4_perm == trainNum) | (*_LN_0_perm == trainNum);
    // State for waiting an additional tick when not all permissions are received
    state backOff
    --> backOff1;
    // State, which releases the requests for needed tracks
    state backOff1 {
        entry / *_ST_4_req[trainNum] = false;
        entry / *_LN_0_req[trainNum] = false;
    }
    // Transition to repeat requesting permissions procedure
    --> waitForPerm;
    final state gotPerm;
  }
  // Transition to the departure state
  >-> Dep_*_ST;
  // State, which handles the departure of a train
  state Dep_*_ST {
    // Set of entry-Actions with hostcode calls to set tracks, points and signals according to depTrack
    entry / 'railPoint(*,STRAIGHT)';
    entry / 'railSignal(*_LN_0, FWD, RED)';
    entry / 'railTrack(*_LN_0,FWD,trainNum,NORMAL)';
    entry / 'railTrack(*_ST_4,FWD,trainNum,NORMAL)';
    entry depTrack == 1 / 'railSignal(*_ST_1, FWD, GREEN)';
    entry depTrack == 2 / 'railSignal(*_ST_2, FWD, GREEN)';
    entry depTrack == 3 / 'railSignal(*_ST_3, FWD, GREEN)';
    //...
  // Transition to next track segment, if contact is triggered
  } --> *_LN_0 with 'railContact(*_LN_0,0)';
  // ----------------------------------------------------------------------------------------------------------------
  // Set of track segment controlling states such as follows
  // ----------------------------------------------------------------------------------------------------------------
  // Transition to next track segment, if contact is triggered
  state *_LN_0 {
    // Hostcode calls for outputs
    entry / 'println("[trainNum][ST-ST] Entering *_LN_0")';
    entry debug / 'println("[trainNum][ST-ST] Requesting permission for *_LN_1")';
    // Entry-Actions with hostcode calls to set previous signal according to depTrack to RED
    entry depTrack == 1 / 'railSignal(*_ST_1, FWD, RED)';
    entry depTrack == 2 / 'railSignal(*_ST_2, FWD, RED)';
    entry depTrack == 3 / 'railSignal(*_ST_3, FWD, RED)';
    // Requesting the next track segment
    entry / *_LN_1_req[trainNum] = true;
    // Region for handling train driving
    region Travel:
      initial state Entry
      // Transition to continuing state, if permitted
      --> Continue with 'railContact(*_LN_0,0)' & (*_LN_1_perm == trainNum)
      // Transition to slowing down else
      --> Slowdown with 'railContact(*_LN_0,0)';
      // State for slowing down the train
      state Slowdown {
        entry debug / 'println("[trainNum][ST-ST] Slowing down on *_LN_0")';
        // Entry-Action with hostcode calls for slowing down the train
        entry / 'railTrack(*_LN_0,FWD,trainNum,CAUTION)';
      }
      // Transition to waiting state
      --> Waiting with 'railContact(*_LN_0,1)'
      // Transition to continuing state, if permitted
      --> Continue with *_LN_1_perm == trainNum;
      // State for train waiting on permission
      state Waiting {
        entry debug / 'println("[trainNum][ST-ST] Stopping on *_LN_0")';
        // Entry-Action with hostcode call for stopping the train
        entry / 'railTrackBrake(*_LN_0)';
      }
      --> Continue with *_LN_1_perm == trainNum;
      // State to continuing driving on the track
      final state Continue {
        entry debug / 'println("[trainNum][ST-ST] Continuing on *_LN_0")';
        // Entry-Actions with hostcode calls to set tracks and signals for driving
        entry / 'railSignal(*_LN_0,FWD,GREEN)';
        entry / 'railTrack(*_LN_0,FWD,trainNum,NORMAL)';
        entry / 'railTrack(*_LN_1,FWD,trainNum,NORMAL)';
        entry / 'railSignal(*_LN_1, FWD, RED)';
      };
    // Region for handling cleanup functionalities
    region Cleanup:
      initial state Entry
      // Transition to cleanup state
      --> cleanup with 'railContact(*_LN_0,0)';
      // State for cleaning up the previous track segments
      final state cleanup {
        entry debug / 'println("[trainNum][ST-ST] Entered *_LN_0 completely")';
        // Entry-Action with hostcode call to switching off the previous track
        entry / 'railTrackOff(*_ST_4)';
        // Entry-Action to release the previous track
        entry / *_ST_4_req[trainNum] = false;
      };
  // Transition to transitional state
  }>-> *_LN_0_*_LN_1;
  state *_LN_0_*_LN_1
  // Transition to next track segment, if contact is triggered
  --> *_LN_1 with 'railContact(*_LN_1,0)';
  // ----------------------------------------------------------------------------------------------------------------
  // State for entering a station
  state *_LN_5 {
    // Variable for checking all needed permissions
    int perm_all_next_segments = false;
    entry / 'println("[trainNum][ST-ST] Entering *_LN_5")';
    entry / 'railSignal(*_LN_4, FWD, RED)';
    // Region for handling train driving such as above,
    // only with perm_all_next_segments for permitting more than one track
    region Travel:
      initial state Entry
      --> Continue with 'railContact(*_LN_5,0)' & perm_all_next_segments
      --> Slowdown with 'railContact(*_LN_5,0)';
      state Slowdown {
        entry debug / 'println("[trainNum][ST-ST] Slowing down on *_LN_5")';
        entry / 'railTrack(*_LN_5,FWD,trainNum,CAUTION)';
      }
      --> Waiting with 'railContact(*_LN_5,1)'
      --> Continue with perm_all_next_segments;
      state Waiting {
        entry debug / 'println("[trainNum][ST-ST] Stopping on *_LN_5")';
        entry / 'railTrackBrake(*_LN_5)';
      }
      --> Continue with perm_all_next_segments;
      final state Continue {
        entry debug / 'println("[trainNum][ST-ST] Continuing on *_LN_5")';
        entry i_arrOnTrack == 1 / 'railTrack(*_ST_1,FWD,trainNum,NORMAL)';
        entry i_arrOnTrack == 2 / 'railTrack(*_ST_2,FWD,trainNum,NORMAL)';
        entry i_arrOnTrack == 3 / 'railTrack(*_ST_3,FWD,trainNum,NORMAL)';
        //...
        entry / arrTrack = i_arrOnTrack;
      };
    // Region for handling cleanup-functionalities such as above
    region Cleanup:
      initial state Entry
      --> cleanup with 'railContact(*_LN_5,0)';
      final state cleanup {
        entry debug / 'println("[trainNum][ST-ST] Entered *_LN_5 completely")';
        entry / 'railTrackOff(*_LN_4)';
        entry / *_LN_4_req[trainNum] = false;
      };
    // Region for handling permissions of all needed tracks
    region Permissions:
      // State for requesting all needed tracks according to destination track and cleanup-Flag
      initial state checking {
        entry / *_ST_0_req[trainNum] = true;
        entry destTrack == 1 | !cleanup / *_ST_1_req[trainNum] = true;
        entry destTrack == 2 | !cleanup / *_ST_2_req[trainNum] = true;
        entry destTrack == 3 | !cleanup / *_ST_3_req[trainNum] = true;
      }
      // Transitions for permitted tracks match wished tracks
      --> success with destTrack == 1 & *_ST_0_perm == trainNum & *_ST_1_perm == trainNum / i_arrOnTrack = 1
      --> success with destTrack == 2 & *_ST_0_perm == trainNum & *_ST_2_perm == trainNum / i_arrOnTrack = 2
      --> success with destTrack == 3 & *_ST_0_perm == trainNum & *_ST_3_perm == trainNum / i_arrOnTrack = 3
      // Transitions for permitted tracks don't match wished tracks
      --> success with *_ST_0_perm == trainNum & *_ST_1_perm == trainNum / i_arrOnTrack = 1
      --> success with *_ST_0_perm == trainNum & *_ST_2_perm == trainNum / i_arrOnTrack = 2
      --> success with *_ST_0_perm == trainNum & *_ST_3_perm == trainNum / i_arrOnTrack = 3
      // Transition for not all tracks permitted
      --> resolving with *_ST_0_perm == trainNum | *_ST_3_perm == trainNum | *_ST_2_perm == trainNum | *_ST_1_perm == trainNum;
      // State for waiting an additional tick
      state resolving
      --> resolving1;

      // State for releasing track requests
      state resolving1 {
        entry / *_ST_0_req[trainNum] = false;
        entry / *_ST_1_req[trainNum] = false;
        entry / *_ST_2_req[trainNum] = false;
        entry / *_ST_3_req[trainNum] = false;
      }
 // Transition for trying the requesting again
      --> checking;
      // State for waiting an additional tick
      state success
      --> success1;
      // State for releasing not used track requests
      final state success1 {
        entry !(i_arrOnTrack == 1) / *_ST_1_req[trainNum] = false;
        entry !(i_arrOnTrack == 2) / *_ST_2_req[trainNum] = false;
        entry !(i_arrOnTrack == 3) / *_ST_3_req[trainNum] = false;
        // Settting perm_all_next_segments to true
        entry / perm_all_next_segments = true;
      };
  // Transition to station entry states
  }>-> *_LN_5_*_ST;
  // State waiting for station entry
  state *_LN_5_*_ST
  --> Arr_*_ST with i_arrOnTrack == 1 & 'railContact(*_ST_1,0)'
  --> Arr_*_ST with i_arrOnTrack == 2 & 'railContact(*_ST_2,0)'
  --> Arr_*_ST with i_arrOnTrack == 3 & 'railContact(*_ST_3,0)';
  // State for setting tracks, points and signals according to i_arrOnTrack
  // and releasing previous track request
  state Arr_*_ST {
    entry / 'railSignal(*_LN_5, FWD, RED)';
    entry / 'railTrackOff(*_LN_5)';
    entry / 'railTrack(*_ST_0,FWD,trainNum,SLOW)';
    entry i_arrOnTrack == 1 / 'railTrack(*_ST_1,FWD,trainNum,SLOW)';
    entry i_arrOnTrack == 2 / 'railTrack(*_ST_2,FWD,trainNum,SLOW)';
    entry i_arrOnTrack == 3 / 'railTrack(*_ST_3,FWD,trainNum,SLOW)';
    entry / *_LN_5_req[trainNum] = false;
    initial state SlowEntry
    --> Slow with i_arrOnTrack == 1 & 'railContact(*_ST_1,0)'
    --> Slow with i_arrOnTrack == 2 & 'railContact(*_ST_2,0)'
    --> Slow with i_arrOnTrack == 3 & 'railContact(*_ST_3,0)';
    // State for switching off previous track and releasing the request
    state Slow {
      entry / 'railTrackOff(*_ST_0)';
      entry / *_ST_0_req[trainNum] = false;
    }
    // Transitions to halt state, when train is at second contact of a track segment
    --> Halt with i_arrOnTrack == 1 & 'railContact(*_ST_1,1)'
    --> Halt with i_arrOnTrack == 2 & 'railContact(*_ST_2,1)'
    --> Halt with i_arrOnTrack == 3 & 'railContact(*_ST_3,1)';

    final state Halt {
      // Entry-Actions for braking the train on correct track
      entry i_arrOnTrack == 1 / 'railTrackBrake(*_ST_1)';
      entry i_arrOnTrack == 2 / 'railTrackBrake(*_ST_2)';
      entry i_arrOnTrack == 3 / 'railTrackBrake(*_ST_3)';
      // Entry-Actions for waiting for timer on correct track
      entry i_arrOnTrack == 1 / 'railArrival(trainNum, *_ST_1)';
      entry i_arrOnTrack == 2 / 'railArrival(trainNum, *_ST_2)';
      entry i_arrOnTrack == 3 / 'railArrival(trainNum, *_ST_3)';
    };
  }
  >-> done;
  state done
  // Transition to final state, if timer is ready
  --> reallyDone with 'railDeparture(trainNum)';
  final state reallyDone;
}
## Dynamic Controller
The dynamic controller handles all 11 Trains. For each train the controller has a region with a referenced dynamic scheduling. Thereby each train can follow an arbitrary schedule. Additionally the controller has a region for stable cleanup function.
//
// Dynamic controller for 11 trains
//
scchart DynamicController11 {
  // Set of request variables for all tracks for 11 trains
  bool IC_JCT_0_req[11], IC_LN_0_req[11], IC_LN_1_req[11], IC_LN_2_req[11];
  bool IC_LN_3_req[11], IC_LN_4_req[11], IC_LN_5_req[11], IC_ST_0_req[11];
  bool IC_ST_1_req[11], IC_ST_2_req[11], IC_ST_3_req[11], IC_ST_4_req[11];
  bool IO_LN_0_req[11], IO_LN_1_req[11], IO_LN_2_req[11], KH_LN_0_req[11];
  bool KH_LN_1_req[11], KH_LN_2_req[11], KH_LN_3_req[11], KH_LN_4_req[11];
  bool KH_LN_5_req[11], KH_LN_6_req[11], KH_LN_7_req[11], KH_LN_8_req[11];
  bool KH_ST_0_req[11], KH_ST_1_req[11], KH_ST_2_req[11], KH_ST_3_req[11];
  bool KH_ST_4_req[11], KH_ST_5_req[11], KH_ST_6_req[11], KIO_LN_0_req[11];
  bool KIO_LN_1_req[11], OC_JCT_0_req[11], OC_LN_0_req[11], OC_LN_1_req[11];
  bool OC_LN_2_req[11], OC_LN_3_req[11], OC_LN_4_req[11], OC_LN_5_req[11];
  bool OC_ST_0_req[11], OC_ST_1_req[11], OC_ST_2_req[11], OC_ST_3_req[11];
  bool OC_ST_4_req[11], OI_LN_0_req[11], OI_LN_1_req[11], OI_LN_2_req[11];
  bool req_in_R , req_out_R , req_in_L , req_out_L;

  // Set of permission variables for all tracks
  int IC_JCT_0_perm, IC_LN_0_perm, IC_LN_1_perm, IC_LN_2_perm;
  int IC_LN_3_perm, IC_LN_4_perm, IC_LN_5_perm, IC_ST_0_perm;
  int IC_ST_1_perm, IC_ST_2_perm, IC_ST_3_perm, IC_ST_4_perm;
  int IO_LN_0_perm, IO_LN_1_perm, IO_LN_2_perm, KH_LN_0_perm;
  int KH_LN_1_perm, KH_LN_2_perm, KH_LN_3_perm, KH_LN_4_perm;
  int KH_LN_5_perm, KH_LN_6_perm, KH_LN_7_perm, KH_LN_8_perm;
  int KH_ST_0_perm, KH_ST_1_perm, KH_ST_2_perm, KH_ST_3_perm;
  int KH_ST_4_perm, KH_ST_5_perm, KH_ST_6_perm, KIO_LN_0_perm;
  int KIO_LN_1_perm, OC_JCT_0_perm, OC_LN_0_perm, OC_LN_1_perm;
  int OC_LN_2_perm, OC_LN_3_perm, OC_LN_4_perm, OC_LN_5_perm;
  int OC_ST_0_perm, OC_ST_1_perm, OC_ST_2_perm, OC_ST_3_perm;
  int OC_ST_4_perm, OI_LN_0_perm, OI_LN_1_perm, OI_LN_2_perm;
  bool perm_in_R , perm_out_R , perm_in_L , perm_out_L;
  // Flags needed for stable cleanup function
  //----------------------------------------------------------------------------------------
  // Flags for trains are ready and back at home
  bool trainDone[11];
  // Flags for trains are on their home circle
  bool circle[11];
  // Flag for trains 0 to 7 are back at home and trains 8 to 10 are on their home circle
  bool mainDone;
  // Flag for all trains are back at home
  bool allDone;
  //----------------------------------------------------------------------------------------
  // Debug flag for additional output
  bool debug;
  // Cleanup flag for halting the trains at home station tracks
  bool cleanup;
  // Variable, that gives the number of trains to C-Controller for stability check
  int trainCount;
  // Constant needed for binding to referenced SCCharts
  const bool c_TRUE = true;
  // State initializing the trains on corresponding tracks
  initial state init references initRailway11Trains
  >-> run;

  // State handling the train schedules
  state run {
    // Region handling the cleanup function
    region Abort:
      initial state notDone
      // Transition when trains 0 to 7 are back at home and trains 8 to 10 are on their home circle
      --> mainDone with trainDone[0] & trainDone[1] & trainDone[2]
          & trainDone[3] & trainDone[4] & trainDone[5]
          & trainDone[6] & trainDone[7]
          & circle[8] & circle[9] & circle[10];

      // State for allowing trains 8 to 10 to halt on the home track
      state mainDone
      --> quitCircle with / mainDone = true;

      // State waiting for trains 8 to 10 halt and setting flag for terminate the controller
      state quitCircle
      --> done with trainDone[8] & trainDone[9] & trainDone[10] / allDone = true;

      final state done;

    // Regions handling the mutual exclusion on the track segments
    region Mutexes:
      initial state Mutexes references mutexRailway11Trains
      // terminates with a strong abort when all trains are at home
      o-> done with allDone;

      final state done;

    region KH_Mutexes:
      initial state KH_Mutexes references kh_mutex
      // terminates with a strong abort when all trains are at home
      o-> done with allDone;

      final state done;
    // Regions that contain the dynamic schedules for trains 0 to 7
    //--------------------------------------------------------------------------------------
    // Region with the dynamic schedule for train 0
    region Train0:
      initial state Train0 {
        @alterHostcode
        const int trainNum = 0
        // Variable for saving the home track
        int homeTrack = 1;
        // Variable for saving the home station
        int homeStation = 1;

        // State referenced to dynamic scheduling
        initial state drive
          references DynamicSheduling
            // Binding circleDone to true for halting at home if cleanup is set
            bind circleDone to c_TRUE
        // Set a flag and a light for train at home
        >-> done with / 'railLight(10,1)'; trainDone[0] = true;

        final state done;
      }
      >-> done;

      final state done;
    // ... (other regions for trains 1 to 7 such as before)
    //--------------------------------------------------------------------------------------
    // Regions that contain the dynamic schedules for trains 8 to 10
    // Differences to regions above is that the trains 8 to 10 circle at home station circle
    // until trains 0 to 7 are back at home station and track
    // For this circleDone binds mainDone flag
    //--------------------------------------------------------------------------------------
    // Region with the dynamic schedule for train 8
    region Train8:
      initial state Train8 {
        @alterHostcode
        const int trainNum = 8
        // Variable for saving the home track
        int homeTrack = 5;
        // Variable for saving the home station
        int homeStation = 1;

        // State referenced to dynamic scheduling
        initial state drive
          references DynamicSheduling
            // Binding circleDone to mainDone for halting at home only if cleanup is set
            // and trains 0 to 7 are at home and 8 to 10 on home circle
            bind circleDone to mainDone
       // Set a flag and a light for train at home
       >-> done with / 'railLight(6,1)'; trainDone[8] = true;

        final state done;
      }
      >-> done;

      final state done;
      // ... (other regions for trains 9 and 10 such as before)
      //--------------------------------------------------------------------------------------
 }
  >-> flash;

  // State for flashing the lights at the end of the controller
  state flash
  --> done with / 'railFlashLight()';

  final state done;
}
### Dynamic Scheduling
Each train has the same dynamic scheduling. The basic idea are 4 station-states (KH, KHr, IC, OC). Each time a train is one of these states, the next target station is looked up. Depending on the current station there are 4 different travel paths available each leading into in of the 4 station-states. This way the dynamic scheduling can handle every possible schedule for each train.
In addition to the travel paths each station-state has a cleanup-transition. A train can only enter cleanup mode, when he arrived at his target station. Each train has a homestation and a hometrack, which he travels to once cleanup is started. Upon arriving at their hometrack, the train shuts down. Once every train is shut down, cleanup finished and every train is back at his starting position. Every station has one track, which does not allow the train, who wants to travel to that track, to shut down. These are KH_ST_5, IC_ST_1 and OC_ST_3. The trains traveling to these stations have to drive circles at KH_LN, IC_LN or OC_LN. Once these are the only trains driving, they are allowed to shut down too. This way a station can not block trains to drive through this station by shutting down all trains in that station.